 init(uint8_t xtal_load_c, uint32_t ref_osc_freq, int32_t corr)
*
* Setup communications to the Si5351 and set the crystal
* load capacitance.
*
* xtal_load_c - Crystal load capacitance. Use the SI5351_CRYSTAL_LOAD_*PF
* defines in the header file
* xo_freq - Crystal/reference oscillator frequency in 1 Hz increments.
* Defaults to 25000000 if a 0 is used here.
* corr - Frequency correction constant in parts-per-billion
*
* Returns a boolean that indicates whether a device was found on the desired
* I2C address.
*
*/
bool Si5351::init(uint8_t xtal_load_c, uint32_t xo_freq, int32_t corr)
{
// Start I2C comms
Wire.begin();
// Check for a device on the bus, bail out if it is not there
Wire.beginTransmission(i2c_bus_addr);
uint8_t reg_val;
 reg_val = Wire.endTransmission();
if(reg_val == 0)
{
// Wait for SYS_INIT flag to be clear, indicating that device is ready
uint8_t status_reg = 0;
do
{
status_reg = si5351_read(SI5351_DEVICE_STATUS);
} while (status_reg >> 7 == 1);
// Set crystal load capacitance
si5351_write(SI5351_CRYSTAL_LOAD, (xtal_load_c & SI5351_CRYSTAL_LOAD_MASK) | 0b00010010);
// Set up the XO reference frequency
if (xo_freq != 0)
{
set_ref_freq(xo_freq, SI5351_PLL_INPUT_XO);
}
else
{
set_ref_freq(SI5351_XTAL_FREQ, SI5351_PLL_INPUT_XO);
}
// Set the frequency calibration for the XO
set_correction(corr, SI5351_PLL_INPUT_XO);
reset();
return true;
}
else
{
return false;
}
}
/*
* set_correction(int32_t corr, enum si5351_pll_input ref_osc)
*
* corr - Correction factor in ppb
* ref_osc - Desired reference oscillator
* (use the si5351_pll_input enum)
*
* Use this to set the oscillator correction factor.
* This value is a signed 32-bit integer of the
* parts-per-billion value that the actual oscillation
* frequency deviates from the specified frequency.
*
* The frequency calibration is done as a one-time procedure.
* Any desired test frequency within the normal range of the
* Si5351 should be set, then the actual output frequency
* should be measured as accurately as possible. The
* difference between the measured and specified frequencies
* should be calculated in Hertz, then multiplied by 10 in
* order to get the parts-per-billion value.
*
* Since the Si5351 itself has an intrinsic 0 PPM error, this
* correction factor is good across the entire tuning range of
* the Si5351. Once this calibration is done accurately, it
* should not have to be done again for the same Si5351 and
* crystal.
*/
void Si5351::set_correction(int32_t corr, enum si5351_pll_input ref_osc)
{
ref_correction[(uint8_t)ref_osc] = corr;
// Recalculate and set PLL freqs based on correction value
set_pll(plla_freq, SI5351_PLLA);
set_pll(pllb_freq, SI5351_PLLB);
}